## Slide 1: Compound Helicopter – Individual Assignment 2
Name:
Roll Number:

## Slide 2: Section 1: Additional Assumptions & Data

## Slide 3: 1.1 Individual Assumptions/Data
In custom helicopter, it is assumed that conditions on both rotors are identical Modelling this is done as follows: The weight and power is divided in half, while the resultant power and thrust and torque is mutliplied by two. Essentially two half helecopters glued together working independently Additionally, since antisymmetric moments are generated, the net moment moment normal to the tip path plane cancels out almost perfectly The trims are chosen to cancel out the other two moment directions

## Slide 4: 1.2: Rough schematic sketch of own compound helicopter
Note: Helicopter Design (Individual)

## Slide 5: Section 2: Updated Helicopter Design

## Slide 6: 2.1: Design Parameters of your updated Design
 | Rotor 1 | Rotor 2 | Rotor …
Rotor Description (role) | Main Rotor 1 | Main Rotor 2 | 
Airfoil | 2412 | 2412 | 
Rotor Radius (m) | 16m | 16m | 
Rotor Speed (m) | Variable | Variable | 
Number of Blades | 3 | 3 | 
Chord Length Variation | 0.9- 0.8 | 0.9-0.8 | 
Twist Variation | 2deg per meter | 2deg per meter | 
Root Cutout | 0.4m | 0.4m | 

## Slide 7: Section 3: Trim Settings

## Slide 8: 3.1 Trim settings and resultant forces and moment for 200km/h level flight at 2000 AMSL
θ0 (All are in degrees) | -4.573698366180704 | Fx In Newtons | 0
θ1s | 10.461857920418048 | FY | -27.99360724761209
θ1c | 0.6439573809240575 | FZ | 0
θ0,t | -1.0 | MX in Newton-M | -1.1786887538864856
αTPP | 11.592860908427829 | MY | 30106.748140726868 (Note, this is equal to zero due to symmetry)
Any Other inputs |  | MZ | -4.169519571674788
 |  | β0 | 0.38065974027793115

## Slide 9: Section 4: Forward Flight Mission Test

## Slide 10: Findings for your compound helicopter design at 2000 m AMSL
4.1 Maximum Speed based on blade stall | 110 m/s
4.2 Maximum Speed based on power requirement | 130 m/s
4.3 Maximum Range | 639.6 km in 2.0 hours
4.4 Maximum Endurance | 2.3 hours

## Slide 11: Section 5 : Bonus Task : Flight Simulator Development

## Slide 12: 5.1 Placement of components and C.G. w.r.t. Helicopter nose
Component | X | Y | Z
Assumed C.G | 12 | 1 | 0
Rotor 1 | 20 | 1 | 0
Rotor 2 | 1 | 1 | 0
Rotor… |  |  | 
Wing/Stabilizer - 1 | NA | NA | NA
Wing/Stabilizer - 2 | NA | NA | NA
Actuator – 1 | NA | NA | NA
Actuator – 2 | NA | NA | NA

## Slide 13: 5.2 Algorithm of the simulator augmented for forward flight

## Slide 14: 5.3: Video Clip of Flight Simulator

## Slide 15: 5.4: Observations from Simulations
Comments / Observations
…

## Slide 16: Acknowledgement
< Mandatory to acknowledge people you discussed with or took help for any part of the assignment>

## Slide 17: References
< List all references (books, paper, websites, etc.) used while doing the assignment>